## Slide 1
Real-Time Operating System for Traffic Signal Control
Technical Presentation
OS Type • Structure • System Calls
1
Presented By:
Dharshini(192521408)
CSA0408-Operating System

## Slide 2
1. Type of OS Used and Justification
A traffic signal controller is a time-critical embedded system
REAL-TIME OPERATING SYSTEM (RTOS)
Example: FreeRTOS
• Signal changes must happen at predictable times.
• The system must respond quickly to sensor events.
• Multiple tasks can run: signal control, sensor reading and monitoring.
• Task priorities allow urgent events to receive CPU time quickly.
Predictable response
2

## Slide 3
2. OS Structure
The RTOS sits between the traffic-control application and the hardware
TRAFFIC SIGNAL APPLICATION
Signal Control Task
Sensor Task
Monitoring Task
Timer Task
RTOS KERNEL
Scheduler
Task Management
Queues / Semaphores / Timers
3

## Slide 4
3. Main OS Components
What each RTOS component does in the traffic controller
Scheduler
Chooses which task runs next.
Tasks
Separate activities such as sensing and signal control.
Queues
Pass data/events between tasks.
Semaphores
Synchronize access to shared resources.
Timers
Generate time-based events.
Interrupt handling
Respond quickly to hardware events.
4

## Slide 5
4. System Calls for Process / Task Control
FreeRTOS uses kernel APIs to create and control tasks
xTaskCreate()
Create a task
vTaskStartScheduler()
Start the RTOS scheduler
taskYIELD()
Give another ready task a chance to run
vTaskSuspend()
Temporarily stop a task
vTaskResume()
Allow a suspended task to run again
xQueueSend() / xQueueReceive()
Communicate events or data between tasks
5

## Slide 6
5. System Calls / APIs for Timing
Timing APIs control how long signal phases and periodic tasks run
GREEN 30 seconds
AMBER 15 seconds
RED 30 seconds
vTaskDelay()
• Blocks the current task for a specified time.
• The CPU can run another ready task during the delay.
Software Timers
• Useful for periodic actions.
• RTOS ticks provide the basic time reference.
6